-

Raport
PBL

### Christopher Lozinski
Paweł Orszulik
Łukasz Fuss
1. Projektem realizowanym w ramach PBL było stworzenie modelu procesora opierającego się na instrucjach podanych w normie:
IEC 61131-3: Programming Industrial Automation Systems.
Oraz przeprowadzenie jego syntezy oraz przetestowanie jego działania na DE1-SoC.
2. Założenia projektowe:
- instrukcje są trójargumentowe
- zaprojektowany procesor ma być jednocyklowy jeśli ogranicznia technologiczne na to pozwolą

3. Lista instrukcji zaprojektowanego procesora:

Struktura 40 bitowej intrukcji:

- 8 bitowy kod operacji
- 8 bitowy adres pamięci, rejestru lub wartość danej natychmiastowej (źródło 1)
- 8 bitowy adres pamięci, rejestru lub wartość danej natychmiastowej (źródło 2)
- 8 bitowy adres pamięci lub rejestru (adres zapisu wyniku oparacji)
- 2 wolne bity
- 2 bity kodujące miejsce odczytu żródła 1
- 2 bity kodujące miejsce odczytu żródła 2
- 2 bity kodujące miejsce zapisu wyniku operacji
Możliwe kody miejsca odczytu lub zapisu:
- 00	rejestry
- 01	pamięć bitowa
- 10	pamięć słów
- 11	dana natychmiastowa (tylko w przypadku odczytu)
4. Schemat procesora:

5. Opis poszczególnych modułów:
Jednostka arytmetyczno-logiczna – ALU
Zadaniem tego układu kombinacyjnego jest wykonywanie operacji arytmetycznych, logicznych i zarządzania pamięcią RAM. Wewnętrzna logika wypracowuje odpowiedni wynik dla dwóch argumentów wejściowych i wybranej operacji(przez sygnał op_code). ALU przesyła stan flag Carry(C) i Borrow(B) do rejestru flag. Wartym podkreślenia jest sposób wyboru źródła argumentów wejściowych, dla wejścia in_a i in_b możemy odczytać wartość zmiennej z czterech źródeł zależnie od sygnałów source1_choice i source2_choice. Poniżej opisana jest zależność między sygnałem sourceX_chioce(X może być równe 1 albo 2) a źródłem zmiennej:
sourceX_choice	Źródło
00	Rejestry
01	Pamięć RAM Bit
10	Pamięć RAM Word
11	Zmienna natychmiastowa

Rejestr Flag – Flag Reg
W tym rejestrze zatrzaskiwany jest stan flag Zero(Z), Carry(C) i Borrow(B).
Flaga Z informuje o wystąpieniu zera w rejestrze R2. Zatrzaskiwanie stanu flagi Z przy opadającym zboczu zegara pozwala na zaktualizowanie stanu flagi pół cyklu zegara wcześniej. Reszta układu jest zsynchronizowana z narastającym zboczem. Takie rozwiązanie jest konieczne do realizacji skoków w programie opartych o zawartość akumulatora(rejestr R2) w mikroprocesorze jednocyklowym.
W naszym mikroprocesorze każda instrukcja potrzebuje dokładnie jednego taktu zegara do poprawnego wykonania się. Na przykład instrukcja IF0JUMP wykona skok do podanego adresu kiedy flaga Z jest równa 1 - zero w akumulatorze. Pod uwagę brany jest stan flagi Z przed narastającym zboczem z zachowaniem czasów setup i hold. Jeśli w instrukcji poprzedzającej IF0JUMP doszło do zmiany stanu flagi Z to stan tej flagi w rejestrze flag zostanie odpowiednio szybko zaktualizowany tylko wtedy, kiedy rejestr flag jest zsynchronizowanym z opadającym zboczem. Użycie narastającego zbocza wymagało by odczekania jednego taktu zegara w celu odczytania przez IF0JUMP oczekiwanej przez programistę wartości flagi Z.
Flagi C i B są aktualizowane tylko jeśli ALU wysteruje sygnał flag_cb_valid i wystąpi narastające zbocze zegara. Pozwala to na podtrzymanie stanu flag C i B na czas dłuższy niż jeden takt zegara.
Wszystkie flagi można wyzerować sygnałem flag_rst.
Pamięć operacyjna bitowa - RAM Bit
Pamięć operacyjna bitowa została dodana do naszego mikroprocesora w celu realizacji obsługi wejść i wyjść. Rozmiar pamięci to 256 bitów. Posiada dwie bramy pozwalające na odczyt pamięci i jedną bramę pozwalającą na zapis. W symulacji używany jest model tej pamięci napisany w Verilogu. Do syntezy użyto dedykowanej, dla układu FPGA Intel Altera Cyclone V, pamięci RAM z katalogu IP Core. Ta pamięć bazuje na blokach pamięci MLAB, które znajdują się fizycznie w układzie FPGA. Niestety w katalogu IP Core Intela nie występuje wersja trójbramowa pamięci RAM. Dlatego do skonstruowania jednej pamięci RAM z dwoma bramami czytającymi i jedną zapisującą, użyto dwóch bloków pamięci MLAB. W celu zapewnienia spójności danych, do obu bloków wykonywany jest jednoczesny zapis.
Zewnętrzny układ jest odpowiedzialny za odczyt stanu wejść fizycznych i zapisanie tych stanów w konkretnych adresach pamięci RAM Bit. Drugim zadaniem tego układu jest odczytanie stanu komórek pamięci RAM Bit, przeznaczonych do ustawiania stanu wyjść przez mikroprocesor, i ustawienie wyjść fizycznych zgodnie ze stanem tych komórek.
Pamięć operacyjna(8-bit) - RAM Word
Pamięć operacyjna przechowująca zmienne o szerokości 8 bitów. Rozmiar pamięci to 256 8-bitowych słów. Została tak samo skonstruowana jak pamięć RAM Bit, także posiada dwie bramy czytające i jedną bramę zapisującą zmienną do pamięci.

Rejestry - Register File
Jest to zbiór rejestrów operacyjnych. Rejestrów jest 11, każdy o szerokości 8 bitów, z czego programista ma pełny dostęp tylko do 9 z nich. Rejestr R0 na stałe jest równy 8’h00 i pozwala tylko na odczyt tej wartości. Rejestr R1 na stałe przechowuje 8’h11 i zachowuje się jak R0. Rejestr R2 to akumulator(ACC, CR – Current Result), na jego podstawie ustawiana jest flaga Z. W celu spełnienia jednocyklowości tego mikroprocesora, koniecznym było wprowadzenie przewidywania kolejnego stanu flagi Z. Dzieje się to przez analizę czy dana, która przyszła do rejestrów będzie zapisana do R2 i czy jest równa 8’h00. Jeśli tak jest to flaga Z jest ustawiana w stan wysoki mimo, że w R2 może jeszcze nie znajdować się wartość 8’h00. Tym sposobem udało się uniknąć konieczności czekania jednego taktu zegara po zmianie stanu flagi Z jeśli programista chciał wykonać instrukcję np. IF0JUMP. Układ ten posiada także zaimplementowany stos.
Rejestry R3-R10 są ogólnego przeznaczenia. Zbiór rejestrów posiada dwie bramy do odczytywania poszczególnego rejestru i jedną bramę do zapisu do konkretnego rejestru(poza R0 i R1). Wybór konkretnego rejestru odbywa się przez podanie jego adresu(adresy dostępne: 0 - 11 przy odczycie, 2 - 11 przy zapisie)
Licznik programu:
Licznik programów to rejestr procesora zawierający adres następnej instrucji.
Moduł posiada możliwość resetu licznika, skoku na zadany adres instrukcji (adres bezpośredni) oraz skoku na adres powrotu.
ROM (memory moduł):
Moduł zawierający instrukcje procesora realizujące zadany program. Instrukcje są zapisany w pliku .hex i odczytywane w czsie kompilacji modułu.
Dekoder
Moduł dekodujący instrukcje i sterujący skokami warunkowymi jak i bezwarunkowymi oraz skokiem na adres powrotu. Moduł steruje również stosem zapisując stan rejestrów w przypadku skoku z śladem. Ponadto ważną funckcją dekodera jest zdekodowanie instrukcji na kod oparacji, argumenty oraz kody miejsc odczytu żródeł oraz zapisu.
Stos (do zapisu adresów powrotu)
Stos zachowujący adres powrotu w przypadku wykonania instrukcji call.

6. Kod programu testowego
// assemby code for PBL
// compilator ommits empty lines
// to comment line add "//" in front !!IMPORTANT!! NO SPACES BEFORE "//"
//	to add comment at the end of line add "//" followed by your comment
// use def keyword followed by name followed by value
// it works like defines in C so for example:
// def start 00
// AND start 00 02 300
// start in AND operation will be replaced in compilation by 00
//////////////// explanation for current code /////////////////
// r_ prefix register addr
// b_ prefix bit memory addr
// w_ prefix word memory addr
// i_ data_imidiate value in hex
/////////////////////// DEFINE SECTION /////////////////////////////////
def reg_0	00
def reg_1	01
def r_acc	02 // reg addr of acc

def b_start	00 // mem bit addr
def b_stop	01 // mem bit addr ~b_stop resets lamp and timer
def b_max	02 // mem bit addr
def b_lamp	03 // mem bit addr lamp
def b_motor	04 // mem bit addr motor
def b_ack	05 // ack motor started 3 times

def w_pressure	00 // mem word addr
def w_timer 01 // timer register
def w_cnt	02 // counter for counting down motor tests
def w_temp 03 // addr temp
def w_pres_cond 04 // addr checking pressure condition
def w_sub	05 // addr for substraction from timer
def w_sub2	06 // addr for substraction fron counter
def i_80	50 // data imidiate 80%
def i_wait_time 02 // time in clk cycles to count
def i_75	4B // data imidiate 75%
///////////////// setting memory values /////////////////
RST	b_ack	1	//set ack to 0
RST	b_lamp	1	//set initial lamp value to 0
SET	b_start	1	//set start button to 1
SET	b_stop	1	//set stop value to 1 (active state = 0)
SET	b_max	1	//set max value to 1 (active state = 0)
RST	b_motor	1	//set motor driver to 0
OR	reg_0	i_wait_time w_timer	032 //set timer = wait time
OR	reg_0	i_80	w_pressure	032 //set pressure to i_80%
OR	reg_0	02	w_timer	032 //set timer for to cycles
OR	reg_0	03	w_cnt	032 //set motor startup counter to 3 times
///////////////Program////////////////////////////////
RST	w_temp	2	//reset registers
RST	r_acc	0	//reset registers
AND b_stop	b_max	r_acc	110	//Evaluate reset condition
NOT r_acc	r_acc	00	//Evaluate reset condition
LT	w_pressure	i_75	w_pres_cond	232
OR	r_acc	w_pres_cond	r_acc	020
OR	b_lamp	b_start	b_lamp	111 //if start pressed set lamp to 1
ANDN	b_lamp r_acc	b_lamp 101 //if reset codition met then set lamp to 0
LD	b_lamp	1
IF1JUMP 16	//if lamp not active reset timer
OR	reg_0	i_wait_time w_timer	032
LD	w_timer	2
IF0JUMP	1A	//if timer is zero jump over decrementation and set motor to 1
SUB	w_timer	b_lamp	w_timer	212	//decrement timer
JUMP	0B	//start new cycle
SET	b_motor	1
///////////////// edge detection ////////////////////////
RST	w_sub2	2	// reset memory to avoid accidental usage of wrong data
RST	r_acc	0	// reset acc for same reason as above
XOR	b_motor	w_temp	w_sub2	122	// check for edge
AND	w_sub2	b_motor	w_sub2	212	// check for posegde
OR	b_motor	reg_0	w_temp	102	// save previous motor state for egde detection
LD	b_ack	1
IF0JUMP 23 //
OR	reg_0	03	w_cnt	032	// if ack is 1 then reset counter
LD	w_cnt	2
IF0JUMP 26	// if count is not 0 decrement
SUB	w_cnt	w_sub2	w_cnt	222 // decrement couter
LD	w_cnt	2
IF1JUMP	0B	// if couter not 0 then start new cycle
SET	b_max	1	// if counter 0 set max to 1
JUMP 0B	// start new cycle

# Instruction Format
Our assignment was to build a 3 argument CPU where each argument could be a register number, a bit memory address, a word memory address, or an immediate value. That calls for 5 fields, a six bit opcode field, an 8 bit first argument field, a second 8 bit argument field, an 8 bit output field, and a six bit type field. Initially we did not have an assembler, so it was most readable to use hex values, which led to 5 fields each of 2 hex or 8 bits wide, for a total of 40 bits. The extra two bits in the choice field proved useful for allowing iteration.
# Iterative Output Application

An alternative decentralized design was also written. It allowed for the memory address to be read from a specified register, allowing for itteration through arrays. In the end it was not required. Maybe this functionality is less needed for real time control, than in general computing.

All of the opcodes were the same between the two designs. Most of the modules were also the same. In this approach, rather than a centralized controller, logic was devolved to the specific modules. Those modules received copies of the opCode, and were responsible for figuring out how to respond to it. They are described here.

Stack responded to RET, CALL and RST opcodes.

Parser only parses the input instructions and does not operate on the input.

Program Counter responds to RET, CALL, JMP, IF0JUMP, IF1JUMP and RST q

This design also supports iteration by incrementing a register as the memory address. The instruction layout is presented below.

Basically the first two bits on the left, and bit [6] from the right determined if the memory address should be taken from a register. If arg 1 register is TRUE, then the address for argument 1 comes from register [arg1]. If the arg 2 register is TRUE, then the address for argument 2 comes from register [arg2]. If the arg out register is TRUE, then the result is written to the address given in register [argOut]. It turns out that the final project did not need this functionality.

# Iterative Output Results

    INITIALIZING BIT MEMORY
    ADDRESS DATA
      0 1
      1 1
      2 0
      3 1
      .
      .
      .

    INITIALIZING WORD MEMORY
    ADDRESS DATA
      0 0
      1 1
      2 2
      3 3
      .
      .
      .

    BitA WordB Product
    1 0 x
    1 1 0
    0 2 1
    1 3 0
    1 4 3
    .
    .
    .

# Iterative Output Assembly
LD 1 2 030 //Load a 1 into register 2 the accumulator
LD 1 3 030 //Load a 1 into register 3
LD 1 1 031 //Load a 1 into bitMemory addr 1
LD 1 1 032 //Load a 1 into wordMemory addr 1
MUL 1 1 2 120 //Multiply bit memory 4 by word memory 6 into reg 2 accumulator
LD 2 2 030 //Load a 2 into register 2 the accumulator
LD 2 3 030 //Load a 2 into register 3
LD 1 1 031 //Load a 1 into bitMemory addr 1
LD 2 1 032 //Load a 2 into wordMemory addr 1
MUL 2 2 2 120 //Multiply bit memory 4 by word memory 6 into reg 2 accumulator
LD 3 2 030 //Load a 3 into register 2 the accumulator
LD 3 3 030 //Load a 3 into register 3
LD 0 1 031 //Load a 1 into bitMemory addr 1
LD 3 1 032 //Load a 3 into wordMemory addr 1
MUL 3 3 2 120 //Multiply bit memory 4 by word memory 6 into reg 2 accumulator
# PID Controller

To learn about real time control, an 8 bit PID controller was built. First the 32 bit oscillator to be controlled was built. Here is the output of the oscillator.

This is being display in GTKWave. Of course GTKWave has its limitations, It only displays positive values. Meaning that any negative value would look terrible. But the CPU is an 8 bit CPU, so 32 bit to 8 bit data conversion was needed.

   assign positionOut = position[31:24];

Then a PID controller was built. Below is the assembly code. Of course it is really hard to build a PID controller with an 8 bit range. That only gives us +127 to -128. Worse yet, because of the gtkwave limitations, we need to center it on 64 giving not much range of control. Specifically the multipliers for the Integral term has to be 0, or it experiences overflow after 2 or 3 iterations. Similarly the Proportional term is limited to a 1, or again it would experience overflow. Only the derivative term can be a meaningful number.

# PID Controller Assembly

//FIRST DEFINE THE REGISTERS
def positionIn 09
def feedbackOut 08
def position 07
def previousPosition 06
def error 05
def integral 04
def working 03
def result 02
def velocity 01

//NOW DEFINE THE CONSTANTS
def timeStep 01
def setPoint 50 //HEX
def kDerivative FC //THIS IS -4
def kProportional 01
def kIntegral 00 //0 STEP 0

LD positionIn position 00 //1 STEP 1

//CALCULATE THE PROPORTIONAL TERM
SUB position setPoint error 030 //2 08
MUL error kProportional result 030 //3

//CALCULATE THE INTEGRAL TERM
MUL integral kIntegral working 030 //4
ADD working result result 000 //5

//CALCULATE THE DERIVATIVE TERM
SUB position previousPosition velocity 000 //6 08 IS THIS CORRECT
DIV velocity timeStep velocity 030 //7 0A
MUL velocity kDerivative working 030 //8 09
ADD working result result 000 //9 07

//APPLY THE CONTROL SIGNAL
MUL result 01 feedbackOut 030 //10 09

//UPDATE THE INTEGRAL TERM
ADD error integral integral 000

LD position previousPosition 00
JUMP 0

# Conclusion

It was lots of fun working on this processor. 3 argument instructions make coding very easy. But we advise against it. Most modern cpus are 32 bits wide , and most memories are 16/32/64 bits wide.. With this CPU, one would need 3*32 bits of instruction just for the addresses. Plus more for the opcodes and choice fields. That is over 108 bit wide instructions, much too wide for most memories.

And while an 8 bit instruction set was fine for the first assignment, it is recommended to use at least 24 bit instructions for PID controllers.